## Slide 1: Lessons Learned in the Monitoring of EV
Javier Rojas – Project Manager E-Mobility
Energy Evaluation Asia Pacific
Date: 12/10/2023

## Slide 2
> Mi Taxi Eléctrico Program.
> First Experience – Pilot
> Service Scope
> Lessons Learned
Agenda
Energy Evatuation Asia Pacific
Date: 10/10/2023

## Slide 3: Mi Taxi Eléctrico Program
The goal is to trigger the replacement of 50 internal combustión engine (ICE) taxis with electric vehicles (Evs) in the city of Santiago.
The objective is to promote the adoption of e-mobility within the light duty public transportation sector, thereby reducing energy consumption and pollution from high-mileage fleets (>50,000 km/year ~ >30.000 mi/year).
The project involved an investment of $650.000 USD from the Ministry of Energy
Energy Evaluation Asia Pacific

## Slide 4: Benefits of the Program
Purchase of the Vehicle
Energy Evaluation Asia Pacific
Charging Infrastructure
EV Monitoring
1
2
3
Single supplier with a special price for the purchase of 50 units.
Up to $8,600 USD in financing for the purchase (~25%).
Provision of a charger free of charge to the beneficiary.
All registration and energization procedures included.
Real-time data collection from the EV.
Monthly reports on the fleet and each EV performance.

## Slide 5: First Experience – Monitoring Pilot
Before monitoring the EVs of the program, we started with a pilot. We monitored 6 models for 4 months to understand the tecnology.
We looked for startups that had an early-stage work in EV monitoring and experienced companies. We chose a national startup due the flexibility and adaptability of the service.
This experience generated the initial knowledge about EV monitoring within the team. It allowed us to work with flexible timelines and objectives, on partner companies’ EVs.
Energy Evaluation Asia Pacific
Notes: De aquí nacieron los primeros aprendizajes,
- sensores
- tasa de muestreo
- especificaciones de comunicación CAN

## Slide 6: Monitoring the Program’s EVs
We asked for a solution that wouldn't interfere with the vehicle, aiming to preserve the warranty.
The job was done by Movia, a chilean startup focused on data intelligence, who worked in all the tasks of the service.
The know-how of the startup enabled them to decode the CAN specifications and generate specific KPIs for the service required.
Energy Evaluation Asia Pacific
Notes: Esto se realiza por eurística, haciendo pruebas. Se miran los datos y se contrasta con lo que se lee en el tablero.

## Slide 7: Monitoring the Program’s EVs
Data was collected from the CANbus system of the vehicle by contactless devices.
The main indicators we could collect from the CANbus were:
  Speed
  State of Charge
  Odometer
  Voltaje
  Current
  Power
Energy Evaluation Asia Pacific
Notes: Con esto s epueden generar los demás datos

## Slide 8: Lessons Learned - Decoding
The CANbus network produces data every 100 ms. That means 180.000 data points each second (50 EV, 6 variables per vehicle).
Due the amount of data points, the signal behaves as a continuos, but the data collection is discrete.
Because of that, there is a loss of information depending on the moment of the measurement, which can result in discrepancies of up to 20%.
Energy Evaluation Asia Pacific
Example of Current in the EV
Example of Power in the EV
Notes: Ejemplo energía cargada+regenerada y energía consumida.
Integral de la potencia es la energía. Ejemplo de los 2 puntos no mide nada.
Se pierden peaks

## Slide 9: Lessons Learned – Data Analysis
The calculation methodology was proposed by the startup, providing daily data for each vehicle.
While it streamlines daily tasks, it doesn't allow for the analysis of data in shorter intervals and makes it harder to adjust assumptions (e.g. oil price)
Depending on the measurement precision, the obtained values can vary. An example of this is the difference between values obtained by the startup and those obtained with the OEM's measurements.
Energy Evaluation Asia Pacific
Average performance by date
Notes: we couldn’t analyze daily routines of the drivers

## Slide 10: Key Measurements - Energy
Energy Evaluation Asia Pacific
314
MWh charged
107
MWh regenerated
446
MWh consumed
Notes: De aquí nacieron los primeros aprendizajes,
- sensores
- tasa de muestreo
- especificaciones de comunicación CAN

## Slide 11: Key Measurements - Emissions
Energy Evaluation Asia Pacific
123.500
Saved
Liters of Gas
300
Saved
Ton CO2
Notes: De aquí nacieron los primeros aprendizajes,
- sensores
- tasa de muestreo
- especificaciones de comunicación CAN

## Slide 12: Summary
Monitoring EVs funded with tax payer money is key in mesuring the succes of a public policy.
One of the most important steps was the monitoring pilot. That experience gave us the technical knowledge that allowed us to execute the service effectively with our beneficiaries’ cars.
Working with local startups gave us the freedom to adjust the service to our requirements and allowed us to get involved in more technical aspects.
Maintaining consistency in the measurement methodology is crucial for consistent results. Ideally, collaborating with the OEM from the begining is strongly recommended.
Energy Evaluation Asia Pacific
Notes: De aquí nacieron los primeros aprendizajes,
- sensores
- tasa de muestreo
- especificaciones de comunicación CAN

## Slide 13: Lessons Learned in the Monitoring of EV
Javier Rojas
jrojas@agenciaSE.org
Energy Evaluation Asia Pacific
Date: 12/10/2023